## Slide 1: Final Project (Heart Monitor)
Embedded Systems
Arsani Sinout - 900143721

## Slide 2: Project Description
The project requires developing an application that implements an embedded system that uses the STM32 module (connected with USB link) and connected to the ECG sensor module. The application should be running on the PC and should measure the heartbeat rate for 1-minute after the user sets the sampling rate, and show the output in a graphical way.

## Slide 3: Project Components
STM32L432: Nucleo-32
AD8232: ECG Module

## Slide 4: Flow Of Data
Heart Beat Sensor
ECG Module
ADC (STM32)
UART
Output / Storage
Output Processing
Graphical Output

## Slide 5: STM32 Configuration

## Slide 6: Code (C)
int trans_rec = 0;
int srate = 0;
while (1)
{
if (trans_rec == 0)
{
HAL_UART_Receive_IT(&huart2 , (uint8_t *) srate, sizeof(srate));
if (srate > 0)
{
trans_rec = 1;
}

## Slide 7: Code (C)
else
{
HAL_ADC_Start(&hadc1);
res = HAL_ADC_GetValue(&hadc1);
sprintf(out, "%d\r\n", res);
HAL_UART_Transmit(&huart2, (uint8_t*)out, sizeof(out),200);
__HAL_TIM_SET_COUNTER(&htim1,0);
while (__HAL_TIM_GET_COUNTER(&htim1) < 100000 / srate);
}

## Slide 8: Code (Python)
def read():
a=''
while True:
if ser is None:
continue
try:
val = ser.readline().decode("utf-8")
return val
except:
print(" ")

## Slide 9: Code (Python)
ser.port = port
ser.baudrate = int(brate)
ser.bytesize = serial.EIGHTBITS
ser.partiy = serial.PARITY_NONE
ser.timeout = 2
ser.open()
ser.write(srate.encode())
ani = animation.FuncAnimation(fig, animate, fargs=(xs, ys), interval=50)
plt.show()

## Slide 10: UI

## Slide 11: Output

## Slide 12: Thank You